## Slide 1
Workshop II
EnergyPlus Python API Hussein Elehwany – Carleton University

## Slide 2: Agenda
09:00-09:45
  Background on EMS
  Benefits of Python EMS
09:45-10:30
  Running simulation with Jupyter Notebook
  Introducing handles
10:30-10:50: Coffee break
10:50-11:35
  Reading and writing from/to simulation
11:35-12:20
  Hands-on exercise
  Python plugin mode

## Slide 3: About presenter
Hussein Elehwany (He/Him)
Carleton University | 2021-present PhD on utilizing reinforcement learning in occupant-centric controls Supervised by Prof. Gunay & Prof. Ouf
Carl Zeiss, Germany | 2017-2021 Thermal Engineer for precision machinery
Technical University of Munich | 2014-2017 MSc in power engineering

## Slide 4: Software requirements
Python
Jupyter notebook or other IDE
EnergyPlus – version 9.3 or later (recommended version 23 or 24)
Files needed: Github: https://github.com/husseinelehwany/EnergyPlus-python-EMS.git

## Slide 5: EnergyPlus
An open-source whole building energy performance simulation program
Managed by NREL
Some pros
Summary and detailed output
Built-in HVAC and lighting control strategies
User-defined schedules
Extensible runtime scripting system for user-defined control:
  Energy Management System (EMS)

## Slide 6: Energy Management System (EMS)
Using EnergyPlus Runtime Language (ERL)
Access sensor data
Perform high-level control
Change actuators and setpoints

## Slide 7: Why to use Python API ?
Exchange data while a simulation is running.
  Develop routines to manipulate internal variables.
  Call these routines at pre-determined times (e.g., at the start of each HVAC iteration or at every time step, etc.
The ease of using python and utilizing all its libraries.
  Nested loops and user-defined functions
  Objects and data structures, e.g., Numpy & Pandas.
  Developing machine learning models. E.g. Scikit-learn, TensorFlow, PyTorch, etc.

## Slide 8: Simulation timeline without EMS
Simulation Runtime
Preprocessing
Outputs
EnergyPlus Schedule
OR
Temperatures
Energy use
Weather data

## Slide 9: Simulation timeline with EMS
Simulation Runtime
Preprocessing
Outputs
Temperatures
Energy use
Read
temperatures
write
setpoints
Control
method
Weather data

## Slide 10: Modes of using the API
EnergyPlus library
Python plugin
EnergyPlus Python API
run EnergyPlus from Python script
run EnergyPlus using
EP-launch and the simulation calls a python script

## Slide 11: EnergyPlus Python API functions
Runtime API: calls python callback functions from within EnergyPlus at specific points.
Data-transfer API: get sensor and actuator data.
Functional API: fluid and refrigerant property methods.

## Slide 12: Examples of callback functions
callback_after_new_environment_warmup_complete
callback_begin_new_environment
callback_begin_system_timestep_before_predictor
callback_end_system_sizing

## Slide 13: Initialization

## Slide 14: Opening Jupyter Notebook
Download notebook
Open cmd
Go to directory containing notebook file
Type jupyter notebook

## Slide 15: Variable handles
Handles are pointers to point to different EnergyPlus variables and actuators.
Variables called by the script should be defined in the IDF file.
There are 3 types of handles:
  Variable handles.
  Meter handles.
  Actuator handles.

## Slide 16: Actuators via schedules

## Slide 17: Variable handles
Location

## Slide 18: Meter handles

## Slide 19: Good practices
Handles should be read only once
At every time step, actuators should be updated only once

## Slide 20: Hands-on exercise

## Slide 21: References
EnergyPlus Python API documentation: https://nrel.github.io/EnergyPlus/api/python/
Github repository

## Slide 22: Thank You
Questions?
husseinelehwany@cmail.carleton.ca